## Slide 1
bd Systems, Inc. Advanced Technology Division
Waveform Reconstruction via Wavelets By Tom Irvine June 27-29, 2006
Vibrationdata Consulting and Educational Services

## Slide 2: Acknowledgements
The initial funding for this project was provided by
Robin Ferebee
Technical Management
Solid Rocket Booster (SRB) Project Office
Now with NASA/Marshall Space Flight Center
Shock Testing of the SRB IEA Avionics Component
Improving Shock Testing Methods in General
bd Systems · Vibrationdata
NASA is concerned with

## Slide 3: Objectives
Match both measured time domain signal and corresponding SRS for shaker shock testing, using a series of wavelets.
Model other transient pulses with wavelet series.
Be Creative, Think outside the Box
bd Systems · Vibrationdata

## Slide 4: Background
Aerospace & military components are subjected to shock tests
to verify their integrity with respect to shock environments.
The specification format may be:
Drop onto hard surface from prescribed height
MIL-S-901 shock machine
Classical pulse such as half-sine
Shock Response Spectrum (SRS)
SRS is the most common format for launch vehicles.
bd Systems · Vibrationdata

## Slide 5: SRS Animation
Natural Frequencies (Hz):
0.063 0.125 0.25 0.50 1.0 2.0 4.0
Soft
Mount
Hard
Mount
Animation File: HS_SRS.avi Click on image to begin.
Base Input: 1 G, 1 sec Half-sine Pulse

## Slide 6: Shaker Shock
The shock test may be performed on a shaker if the shaker’s frequency and amplitude capabilities are sufficient
A time history must be synthesized to meet the SRS specification
Typically damped sines or wavelets
The net velocity and net displacement must be zero
bd Systems · Vibrationdata

## Slide 7: SRS Synthesis
A series of wavelets can be synthesized to satisfy an SRS specification for shaker shock
Wavelets have zero net displacement and zero net velocity
Damped sines require compensation pulse
Assume control computer accepts ASCII text time history file for shock test in following examples
bd Systems · Vibrationdata

## Slide 8: Wavelet Equation
Wm (t) = acceleration at time t for wavelet m
Am = acceleration amplitude f m = frequency t dm = delay
Nm = number of half-sines, odd integer > 3

## Slide 9: Sample Wavelet

## Slide 10: Innovation
A wavelet series may also be used to reconstruct a time history
(The wavelets are non-orthogonal)
This is done using brute-force curve fitting with random number generation
The resulting series satisfies both the time history and the SRS
bd Systems · Vibrationdata

## Slide 11: Example 1: Single Time History

## Slide 12: Wavelet Series with 3 of 60 Components

## Slide 13: More Synthesized Pulse Time Histories

## Slide 14: Example 1: SRS of Wavelet Series

## Slide 15: Example 1: Conclusion
Wavelet time history can be performed as shaker shock, satisfying both time history and SRS
Add safety margin if appropriate
bd Systems · Vibrationdata

## Slide 16: Multiple Waveforms
The reconstruction method can be extended for the case where multiple measurements are taken in the same axis over a number of accelerometer locations or flights
Spatial and flight-to-flight variation are both concerns
bd Systems · Vibrationdata

## Slide 17: Example 2. Four Measured Time Histories

## Slide 18: P95/50 SRS

## Slide 19: Example 2: Composite Signal Derivation
Add the four signals
Shift time scale and invert amplitudes as necessary to achieve highest GRMS value
Use brute force random number generation
Scaling in next steps will compensate for potential constructive and destructive interference in composite pulse
bd Systems · Vibrationdata

## Slide 20: Example 2: Composite Signal

## Slide 21: Example 2: Synthesis and Scaling Steps
Synthesize a wavelet time history to match composite pulse
Re-scale wavelet parameters so the wavelet SRS satisfies the P95/50 SRS
Brute force random number generation is used for each step
Final time history should “reasonably resemble” the composite of the four original signals
bd Systems · Vibrationdata

## Slide 22: Example 2: Resulting Time History

## Slide 23: Example 2: Time History Comparison

## Slide 24: Example 2: More Time Histories

## Slide 25: Example 2: SRS Comparison

## Slide 26: Example 2: Conclusion
Synthesized wavelet series can be performed as a shaker shock
Both composite pulse and P95/50 SRS are satisfied
bd Systems · Vibrationdata

## Slide 27: Example 3: Pegasus Launch Vehicle
Click Here for Video Link

## Slide 28: Example 3: Payload Dynamic Load
The Pegasus vehicle vibrates like a free-free beam as it is dropped from the L-1011.
The oscillation is a damped sinusoid, with a frequency of about 9 to 10 Hz, depending on the coupled-loads analysis result.
The payload must be designed and preferably tested to withstand this load.
The drop transient cannot be directly performed on a shaker table, however, due to the resulting high net displacement.
Idea: synthesize wavelet series to represent drop transient!
bd Systems · Vibrationdata

## Slide 29: Example 3: Normalized Drop Transient Acceleration

## Slide 30: Example 3: Corresponding Velocity & Displacement

## Slide 31: Future Research
Improve convergence algorithms
Optimize waveforms to minimize peak velocity and displacement while still meeting other goals
Also consider mechanical impedance and force limiting concerns in shock testing
Need an opportunity to test real hardware using this method!
Solution Looking for a Problem
bd Systems · Vibrationdata