## Slide 1: Unit 31
  ISO 2631-1:1997
  Mechanical Vibration and Shock
  Evaluation of Human Exposure to
  Whole-body Vibration

## Slide 2: Human Vibration Concerns
ISO 2631
  Human Health and Comfort
  Probability of Vibration Perception
  Incidence of Motion Sickness
Related concerns
1. Task performance – vision, speech, hand control

## Slide 3: Sources
Vehicles – air, land & sea
Machinery – mining, construction, industry & agriculture

## Slide 4: Rail Vehicles
Primary source of vibration is track irregularities.
Lateral vibration induced by roll is another source. Passengers are usually seated well above center of roll.
Griffin, Human Vibration, p 498
Vibration levels can be reduced by using foam seat cushions.
Griffin, Human Vibration, p 395

## Slide 5: Rail Vehicles Continued
ISO 2631-4:2001
Motion in a fixed-guideway vehicle is characterized by
a) semi-random translational accelerations (in all three axes) and semi-random angular accelerations (about all three axes) due to imperfections in track/wheel surfaces, track alignment errors, etc.,
b) more or less periodic motions due to instability problems (swaying), motions in suspension, long-wave track irregularities, periodic distances between joints, staggered track, etc.,

## Slide 6: Rail Vehicles Continued
ISO 2631-4:2001
c) quasi-static magnitudes of acceleration along both lateral and vertical axes and roll (bank) and yaw motion due to alignment and cant (super-elevation) and quasi-static magnitudes of acceleration along the longitudinal axis due to acceleration or braking of the vehicle, and
d) sudden motions due to large imperfections in track or switches, or changes of quasi-static levels (jerk) due to changes in curve radii with or without transition curves.

## Slide 7: Bus Driver Test Workers’ Compensation Board, B.C., Canada

## Slide 8: Axes
Images courtesy of the Australian Safetyline Institute

## Slide 9: Axes (Continued)

## Slide 10: Weighting Factors
The sensitivity of the body to vibration in each axis is accounted for by multiplying factors.
The frequency-weighted acceleration (m/s²) is multiplied by the weighting factor before its effect is assessed.

## Slide 11: Frequency Domain
0.5 Hz to 80 Hz for health, comfort, and perception
0.1 Hz to 0.5 Hz for motion sickness

## Slide 17: Weighted RMS
Time Domain
Frequency Domain FFT magnitude
where
is peak (m/s^2)

## Slide 18: Calculation Procedure
1. Divide time history into one or more segments
2. Take FFT
3. Apply weights
4. Calculated overall level from weighted FFT
5. Convert to equivalent 8 hour exposure if necessary, as shown in next slide
6. Compare weighted exposure to ISO 2631 Health Guidance Graph

## Slide 19: Equivalent Exposure
Goal is to convert measured data into equivalent 8 hour level, as appropriate.
Two approaches
(1)
(2)

## Slide 21
Software Programs
Convert time history to weighted acceleration | th_weighted
Convert FFT magnitude to weighted acceleration | ftm_weighted.exe
Convert PSD to weighted acceleration | psd_weighted.exe

## Slide 22: Exercise 1
File seat.txt is a synthesized white noise time history.
Assume that seat.txt is measured data in (m/sec^2).
Calculate the weighted level using program th_weighted.exe
Select a weighting function.
Compare results with ISO 2631 Health Graph.
Repeat using other weighting functions.

## Slide 23: Exercise 2
Calculate the power spectral density of seat.txt using program poweri.exe.
Plot the power spectral density using file: a_ms22hz.psd
Calculate the weighted level of the power spectral density output using program psd_weighted.exe.

## Slide 24: Exercise 3
Calculate the FFT magnitude of seat.txt using program poweri.exe.
Plot the power spectral density using file: a_ms2_pk.mag
Calculate the weighted level of the power spectral density output using program FTM_weighted.exe.