## Slide 1
Unit 201
Nastran FEA Base Excitation Response Spectrum
Revision E
Students should already have some familiarity with Femap & Nastran
NX Nastran is used as the solver, but the methods should work with other versions
Unit 200 is a prerequisite

## Slide 2
Introduction
Shock and vibration analysis can be performed either in the frequency or time domain
Continue with plate from Unit 200
Aluminum, 12 x 12 x 0.25 inch
Translation constrained at corner nodes
Mount plate to heavy seismic mass via rigid links
Use response spectrum analysis
SRS is “shock response spectrum”
Compare results with modal transient analysis from Unit 200
The following software steps must be followed carefully, otherwise errors will result
Rigid links

## Slide 3
Procedure, part I
Femap, NX Nastran and the Vibrationdata Matlab GUI package are all used in this analysis
The GUI package can be downloaded from: https://vibrationdata.wordpress.com/
The mode shapes are shown on the next several slides for review

## Slide 4
Femap: Mode Shape 1
The fundamental mode at 117.6 Hz has 93.3% of the total modal mass in the T3 axis
The acceleration response also depends on higher modes

## Slide 5
Femap: Mode Shape 6
The sixth mode at 723 Hz has 3.6% of the total modal mass in the T3 axis
This mode has the highest contribution to the T3 peak acceleration response at the center node to the input shock
This partly is because there is more input energy at this frequency than at the fundamental frequency and also this mode has the highest eigenvector response at the center node

## Slide 6
Femap: Mode Shape 12
The twelfth mode at 1502 Hz has 1.6% of the total modal mass in the T3 axis

## Slide 7
Femap: Mode Shape 19
The 19th mode at 2266 Hz has only 0.3% of the total modal mass in the T3 axis
But it still makes a significant contribution to the acceleration response

## Slide 8
Matlab: Node 1201 Parameters for T3
n | fn (Hz) | Modal Mass Fraction | Participation Factor | Eigenvector
1 | 117.6 | 0.933 | 0.0923 | 13.98
6 | 723.6 | 0.036 | 0.0182 | 22.28
12 | 1502 | 0.017 | 0.0123 | 2.499
19 | 2266 | 0.003 | 0.0053 | 32.22
The Participation Factors & Eigenvectors are shown as absolute values
The Eigenvectors are mass-normalized
Modes 1, 6, 12 & 19 account for 98.9% of the total mass

## Slide 9
Procedure, part II
Response spectrum analysis is actually an extension of normal modes analysis
ABSSUM – absolute sum method
SRSS – square-root-of-the-sum-of-the-squares
NRL – Naval Research Laboratory method
The SRSS method is probably the best choice for response spectrum analysis because the modal oscillators tend to reach their respective peaks at different times according to frequency
The lower natural frequency oscillators take longer to peak

## Slide 10
where is the mass-normalized eigenvector coefficient for coordinate i and mode j
Conservative assumption that all modal peaks occur simultaneously
These equations are valid for both relative displacement and absolute acceleration.
Pick D values directly off of Relative Displacement SRS curve
ABSSUM Method

## Slide 11
These equations are valid for both relative displacement and absolute acceleration.
Pick D values directly off of Relative Displacement SRS curve
SRSS Method

## Slide 12
Femap: Constraints
Delete all constraints, functions, and output sets from previous model
Delete the base mass and rigid links if present
Delete all unused nodes
Resume as follows:
Create constraint set call seismic & edit corner node constraints so that only TX & TY are fixed
The response spectrum setup has some similarities and differences relative to modal transient

## Slide 13
Femap: Added Points and Nodes
Copy center point twice at -3 inch increments in the Z-axis
Place nodes on added points
Node 2402
Node 2403

## Slide 14
Calculate FEA model mass
Select all elements
Result is 0.00913968 lbf sec^2/in
Or 1.6 kg
Copy total mass using Ctrl-C
Femap: Mass

## Slide 15
Define Seismic Mass property
Mass value is model mass x 1e+06
Enter the following number in the mass box 0.00913968*1e+06
The edit box is too small to show complete number
Femap: Seismic Mass

## Slide 16
Node 2403, Seismic Mass
Femap: Seismic Mass Placement

## Slide 17
Femap: Rigid Link no. 1, TZ only
Node 2402, Independent
Four corner nodes are dependent

## Slide 18
Femap: Rigid Link no. 2, TZ only
Node 2403, Independent
Node 2402, Dependent

## Slide 19
Femap: Add Constraints to Current Constraint Set
All DOF fixed except TZ

## Slide 20
Femap: Create New Constraint Set Called Kinematic

## Slide 21
Femap: Add Constraint to Kinematic Set
Constrain TZ
The seismic mass is constrained in TZ which is the response spectrum base drive axis

## Slide 22
Femap: Define Damping Function
Q=10 is the same as 5% Critical Damping

## Slide 23
fn (Hz) | Peak Accel (G)
10 | 10
2000 | 2000
10000 | 2000
Shock Response Spectrum Q=10
Good practice to extrapolate specification down to 10 Hz if it begins at 100 Hz
Because model may have modes below 100 Hz
Aerospace SRS specifications are typically log-log format
So good practice to perform log-log interpolation as shown in following slides
Go to Matlab Workspace and type:
>> spec=[10 10; 2000 2000; 10000 2000]

## Slide 24
Vibrationdata Matlab GUI

## Slide 25
Matlab: Export Data
>> spec=[10 10; 2000 2000; 10000 2000]
Multiply by 386 to convert G to in/sec^2
Save as: srs_Q10.bdf or whatever

## Slide 26
Femap: Import Analysis Model srs_Q10.bdf

## Slide 27
Femap: View Response Spectrum Function

## Slide 28
Femap: View Response Spectrum Function
Change title from TABLED2 to SRS_Q10

## Slide 29
Femap: Define Response Function vs. Critical Damping
For simplicity, the model damping and SRS specification are both Q=10 or 0.05 fraction critical
Function 7 is the SRS specification
Specifications for other damping values could also be entered as functions and referenced in this table, as needed for interpolation if the model has other damping values
Multiple SRS specifications is covered in Unit 202

## Slide 30
Femap: Define Normal Modes Analysis with Response Spectrum

## Slide 31
Femap: Define Normal Modes Analysis Parameters
Solve for 20 modes

## Slide 32
Femap: Define Nastran Output for Modal Analysis

## Slide 33
Femap: SRS Cross-Reference Function
This is the function that relates the SRS specifications to their respective damping cases
“Square root of the sum of the squares”
The responses from modes with closely-spaced frequencies will be lumped together

## Slide 34
Femap: Define Boundary Conditions
Main Constraint function
Base input constraint, TZ for this example

## Slide 35
Femap: Define Outputs
Get output f06 file
Quick and easy to output results at all nodes & elements for response spectrum analysis
Only subset of nodes & elements was output for modal transient analysis due to file size and processing time considerations

## Slide 36
Femap: Export Nastran Analysis File
Export analysis file
Run in Nastran

## Slide 37
Matlab: Vibrationdata GUI

## Slide 38
Matlab: Nastran Toolbox

## Slide 39
Matlab: Response Spectrum Results from f06 File

## Slide 40
Matlab: Response Spectrum Acceleration Results
Center node 1201 has T3 peak acceleration = 475.9 G from response spectrum analysis
Modal transient result from Unit 200 was 461 G for this node

## Slide 41
Node 1201
Node 49
Matlab: Response Spectrum Acceleration Results (cont)
Center node 1201 had T3 peak acceleration = 475.9 G
Edge node 49 had highest T3 peak acceleration = 612.5 G
By symmetry, three other edge nodes should have this same acceleration
But node 1201 had highest displacement and velocity responses

## Slide 42
Matlab: Response Spectrum Results
Maximum Displacements:
node value
T1: 2376 0.00000 in
T2: 931 0.00000 in
T3: 1201 0.10746 in
R1: 1 0.02054 rad/sec
R2: 1 0.02054 rad/sec
R3: 1 0.00000 rad/sec
Maximum velocities:
node value
T1: 2376 0.000 in/sec
T2: 931 0.000 in/sec
T3: 1201 83.665 in/sec
R1: 1 20.246 rad/sec
R2: 1 20.246 rad/sec
R3: 1 0.000 rad/sec
Maximum accelerations:
node value
T1: 2376 0.000 G
T2: 931 0.000 G
T3: 49 612.541 G
R1: 1 116739.700 rad/sec^2
R2: 1 116739.700 rad/sec^2
R3: 1 0.000 rad/sec^2
Maximum Quad4 Stress:
element value
NORMAL-X : 1105 6047.053 psi
NORMAL-Y : 24 6047.053 psi
SHEAR-XY : 50 4798.865 psi
MAJOR PRNCPL: 24 6047.816 psi
MINOR PRNCPL: 1128 4997.801 psi
VON MISES : 50 8400.833 psi

## Slide 43
n | fn (Hz) | PF | Eigen vector | Q | Interpolated SRS (G) | ¦ PF x Eig x Spec ¦ (G) | ¦ PF x Eig x Spec ¦2 (G2)
1 | 117.6 | 0.0923 | 13.98 | 10 | 117.6 | 151.7 | 23027
6 | 723.6 | 0.0182 | -22.28 | 10 | 723.6 | 293.4 | 86093
12 | 1502 | 0.0123 | 2.499 | 10 | 1502 | 46.2 | 2131
19 | 2266 | 0.0053 | 32.22 | 10 | 2000 | 341.5 | 116644
 |  |  |  |  |  | sum = 833 G | sum = 227896 G2
 |  |  |  |  |  |  | sqrt of sum = 477 G
Acceleration Response Check for Node 1201 T3
Center node 1201 had T3 peak acceleration = 475.9 G from the FEA
The FEA value passes the modal combination check

## Slide 44
Vibrationdata GUI

## Slide 45
Vibrationdata Shock Toolbox

## Slide 46
>> spec=[10 10; 2000 2000; 10000 2000]
Vibrationdata SRS Modal Combination

## Slide 47
Vibrationdata SRS Modal Combination Results
SRS Q=10
fn(Hz) Accel(G)
10.0 10.0
2000.0 2000.0
10000.0 2000.0
fn Q=10
(Hz) SRS(G)
117.6 117.6
723.6 723.6
1502 1502
2266 2000
fn Part Eigen SRS Modal Response
(Hz) Factor vector Accel(G) Accel(G)
117.6 0.0923 13.98 117.6 151.7
723.6 0.0182 -22.28 723.6 293.4
1502 0.0123 2.499 1502 46.17
2266 0.0053 32.2 2000 341.3
ABSSUM= 832.7 G SRSS= 477.2 G

## Slide 48
n | fn (Hz) | PF | Eigen vector | Q | Interpolated SRS (G) | ¦ PF x Eig x Spec ¦ (G) | ¦ PF x Eig x Spec ¦2 (G2)
1 | 117.6 | 0.0923 | 9.81 | 10 | 117.6 | 106.5 | 11339
6 | 723.6 | 0.0182 | 17.92 | 10 | 723.6 | 236.0 | 55695
12 | 1502 | 0.0123 | -28.5 | 10 | 1502 | 526.5 | 277230
19 | 2266 | 0.0053 | -16.6 | 10 | 2000 | 176.0 | 30962
 |  |  |  |  |  | sum = 1045 G | sum = 375225 G2
 |  |  |  |  |  |  | sqrt of sum = 613 G
Acceleration Response Check for Node 49 T3
Edge node 49 had T3 peak acceleration = 612.5 G from the FEA
The FEA value passes the modal combination check

## Slide 49
Femap: T3 Acceleration Contour Plot, unit = in/sec^2
Import the f06 file into Femap and then View > Select

## Slide 50
Femap: T3 Velocity Contour Plot, unit = in/sec

## Slide 51
Femap: T3 Translation Contour Plot, unit = inch
This is actually the relative displacement

## Slide 52
Matlab: Response Spectrum Stress Elements
Element 50 had the highest Von Mises stress = 8401 psi
Element 1129 had Von Mises stress = 5001 psi
Element 50
Element 1129
Node 1201
Node 101

## Slide 53
Matlab: Response Spectrum Stress Results

## Slide 54
Femap: Von Mises Stress Contour Plot

## Slide 55
Matlab: Vibrationdata Shock Toolbox

## Slide 56
Matlab: MDOF SRS Stress Analysis for Node 1201
The peak velocity response occurs at center Node 1201
The peak stress occurs near each of the four corners
The stress-velocity calculation accounts for this difference

## Slide 57
E | Elastic modulus
ρ | Mass per volume
[Vn]max | Modal velocity
The stress [σn]max for mode n is:
Stress-Velocity Equation
Ĉ is a constant of proportionality dependent upon the geometry of the structure, often assumed for complex equipment to be 4 < Ĉ < 8
Ĉ ≈ 2 for all normal modes of homogeneous plates and beams

## Slide 58
Matlab: Peak MDOF SRS Stress from Node 1201 velocity
SRS Q=10
fn(Hz) Accel(G)
10.0 10.0
2000.0 2000.0
10000.0 2000.0
fn Q=10
(Hz) SRS(G)
117.6 117.6
723.6 723.6
1502 1502
2266 2000
fn Q Part Eigen Accel PV SRS Modal Response
(Hz) Factor vector SRS(G) (in/sec) stress(psi)
117.6 10 0.0923 13.98 117.6 61.43 8070
723.6 10 0.0182 -22.28 723.6 61.43 2536
1502 10 0.0123 2.499 1502 61.43 192.2
2266 10 0.0053 32.2 2000 54.22 942
ABSSUM= 11740 psi SRSS= 8513.1 psi
The peak FEA response spectrum stress for the whole plate was 8401 psi
FEA stress passes sanity check, but a lower Ĉ value may be justified so that the SRSS agrees more closely with the FEA results

## Slide 59
Future Work
Expand Nastran stress post-processing options in Vibrationdata GUI
Include strain
Please contact Tom Irvine Email: tom@irvinemail.org if you have suggestions or find bugs in the Vibrationdata GUI
Homework
Repeat analysis with triangular plate elements
Experiment with different mesh densities
Repeat analysis with an alternate base input response spectrum
Compare results from Absolute Sum and SRSS methods