## Slide 1
Unit 204
FEA PSD Response for Base Excitation
using Femap, Nastran & Matlab
Students should already have some familiarity with Femap & Nastran
NX Nastran is used as the solver, but the methods should work with other versions

## Slide 2
Introduction
Shock and vibration analysis can be performed either in the frequency or time domain
Continue with plate from Unit 200
Aluminum, 12 x 12 x 0.25 inch
Translation constrained at corner nodes
Mount plate to heavy seismic mass via rigid links
Use “Random Response” analysis
PSD is “power spectral density”
Compare results with modal transient analysis from Unit 203
The following software steps must be followed carefully, otherwise errors will result
Rigid links

## Slide 3
Procedure, part I
Femap, NX Nastran and the Vibrationdata Matlab GUI package are all used in this analysis
The GUI package can be downloaded from: https://vibrationdata.wordpress.com/
The mode shapes are shown on the next several slides for review

## Slide 4
NAVMAT PSD Base Input

## Slide 5
Femap: Mode Shape 1
The fundamental mode at 117.6 Hz has 93.3% of the total modal mass in the T3 axis
The acceleration response also depends on higher modes

## Slide 6
Femap: Mode Shape 6
The sixth mode at 723 Hz has 3.6% of the total modal mass in the T3 axis

## Slide 7
Femap: Mode Shape 12
The twelfth mode at 1502 Hz has 1.6% of the total modal mass in the T3 axis

## Slide 8
Femap: Mode Shape 19
The 19th mode at 2266 Hz has only 0.3% of the total modal mass in the T3 axis
But it still makes a significant contribution to the acceleration response

## Slide 9
Matlab: Node 1201 Parameters for T3
n | fn (Hz) | Modal Mass Fraction | Participation Factor | Eigenvector
1 | 117.6 | 0.933 | 0.0923 | 13.98
6 | 723.6 | 0.036 | 0.0182 | 22.28
12 | 1502 | 0.017 | 0.0123 | 2.499
19 | 2266 | 0.003 | 0.0053 | 32.22
The Participation Factors & Eigenvectors are shown as absolute values
The Eigenvectors are mass-normalized
Modes 1, 6, 12 & 19 account for 98.9% of the total mass

## Slide 10
Femap: Define Damping Function

## Slide 11
FEMAP: Function Definition

## Slide 12
Femap: Define Accel PSD Function
The X-axis unit is Frequency (Hz)
The Y-axis unit is Accel (G^2/Hz)

## Slide 13
Femap: Constraints
Edit corner node constraints so that only TX & TY are fixed

## Slide 14
Copy center point twice at -3 inch increments in the Z-axis
Place node on point at middle point
Node 2402
Femap: Added Points and Node

## Slide 15
Femap: Select Rigid Element

## Slide 16
Femap: Configure Rigid Element, RBE2
Dependent DOF is TZ
Dependent Nodes are the corner nodes
Node 2402 is the independent Node, -3 inch from plate’s center node in Z-axis

## Slide 17
Node 2402
Rigid Link
Femap: Plate with Rigid Element

## Slide 18
Femap: Load Set
Step 1:
Create Load Set
Step 2:
Dynamic Analysis

## Slide 19
Femap: Load Set

## Slide 25
FEMAP: Rigid Connecting Link

## Slide 26
FEMAP: Constrain Base Mass Node
Note that the Z-axis is perpendicular to the plate

## Slide 27
FEMAP: Model with Constraints

## Slide 28
Femap: Node Check
This step may be unnecessary but it is a “good engineering” practice

## Slide 29
Femap: Renumber Nodes

## Slide 30
Femap: Node Group
Node 2402
Node 2403
Node 1
Node 49
Node 1201

## Slide 31
Femap: Element Group
Element 50
Element 1129
Node 1201

## Slide 32
Femap: Random Response

## Slide 33
Femap: Analysis Steps

## Slide 34
Femap: Analysis, Solution Frequencies, etc.

## Slide 35
Femap: Analysis Steps, PSD & Boundary Conditions
PSD Function, previously defined

## Slide 36
Export the analysis model
Run in Nastran
Post-process the f06 file using the Matlab script as shown in the following slides
Femap: Analysis Final Step

## Slide 37
Vibrationdata Matlab GUI

## Slide 38
Vibrationdata: Nastran Toolbox

## Slide 39
Vibrationdata: Nastran PSD Post-processing

## Slide 40
NAVMAT PSD Base Input

## Slide 41
PSD Response at Plate Center Node
This plot agrees with the result obtained in Unit 203

## Slide 42
PSD Response at Plate Mid Edge Node
This plot agrees with the result obtained in Unit 203