## Slide 1
Dynamic Concepts, Inc. Huntsville, Alabama
Vibrationdata
2nd Workshop on Spacecraft Shock Environment and Verification, 19-20 November 2015, ESA-ESTEC, Noordwijk, The Netherlands
Shock Analysis of Launch Vehicle Equipment using Historical Accelerometer Records to Satisfy Shock Response Spectra Specifications
By Tom Irvine Email: tirvine@dynamic-concepts.com

## Slide 2: Introduction - Nonstationary Flight Data
Background
This presentation is extension of an SRB Splashdown shock project with my colleagues Robin Ferebee & Joe Clayton
NASA/TM—2008–215253, An Alternative Method of Specifying Shock Test Criteria
Recent work was prompted by a question from Siamak Ghofranian

## Slide 3: Introduction - Nonstationary Flight Data
The vehicle as mounted on the pad is a tall cantilever beam
Its ability to withstand seismic events must be verified via analysis (NASA-HDBK-7005)
Falcon 9 Launch, Vandenberg AFB

## Slide 4: Introduction - Nonstationary Flight Data
http://a.scpr.org/i/22ebbc723746b0deb523a3e5cf1d687c/75480-full.jpg
California Earthquakes
El Centro 1940
Loma Prieta 1989
San Francisco 1906

## Slide 5: Conclusions
.
Nuclear plant equipment must be tested to seismic shock specifications.
San Onofre Nuclear Power Plant

## Slide 6: Conclusions
.
Generator Subjected to
Seismic Test
This could be an emergency power generator for a hospital in an active seismic zone
Video clip available on YouTube

## Slide 7: Conclusions
.
Design & Testing
Consider the following type of systems & equipment:
  Launch Vehicle & Ground Support Equipment
  Telecommunication
  Medical life-support
  Network servers
  Nuclear power plant control consoles
  Now consider that this equipment is to be installed in an active seismic zone
The equipment must be designed to withstand the dynamic loads and tested if possible
A typical specification format for the loading is the shock response spectrum (SRS)
The testing is performed on a shaker table

## Slide 8: Conclusions
NASA HDBK-7005, Vandenberg AFB
Use the 1% damping (Q=50) curve in the following example

## Slide 9: Conclusions
Time History Synthesis
A time history must be synthesized to satisfy the SRS for testing or transient finite element analysis
  A wide variety of time histories could hypothetically be used including a sine sweep
  But there are concerns about the test article’s linearity, multi-modal response, etc.
  Also concerns about input time history’s skewness, kurtosis, energy, temporal moments, etc.
  Goal is to use a time history which “resembles” a measured strong motion event
  Use a Rube Goldberg method

## Slide 10: Conclusions
El Centro Strong Motion Data

## Slide 11: Conclusions
El Centro NS SRS
20

## Slide 12: Conclusions
SRS Comparison
20
El Centro SRS does not comply with VAFB specification “straight out of the box”
But the El Centro time history can be modified for compliance
Initial slope of the Spec is about
8 dB/octave

## Slide 13: Conclusions
Method Description, part 1
The following steps use trial-and-error-random number generation with some built-in convergence
The method is implemented as a function in the Vibrationdata Matlab GUI package (freely available)
The first step is to decompose the reference time history into a series of wavelets (non-orthogonal shaker shock wavelets)
An acceleration wavelet has zero net velocity and zero net displacement
A series of wavelets likewise has these properties
Wavelets are very amenable to shaker table shock testing and are also convenient for analysis
The examples in this presentation use a series of 200 wavelets to model a reference time history

## Slide 14: Conclusions
.
The second step is to randomly vary the wavelet amplitudes so that the modified wavelet series will have an SRS that matches the specification as closely as possible
The number of iterations may be 16000 or so
The modified time history will thus have some distortion relative to the reference, but this is needed to shape the time history so that its SRS meets the specification
The second step yields an SRS that has some peaks and dips relative to the specification
This is a consequence of trying to adapt a measured time history to a smoothed SRS
Method Description, part 2

## Slide 15: Conclusions
.
Method Description, part 3
The third step is to add wavelets so that the resulting SRS meets the specification within, say, + 3 dB tolerance limits
The third step also adds some distortion
The amount of distortion depends largely on how much the SRS specification differs from that of the reference data

## Slide 16: Conclusions
.
The top time history is the measured El Centro NS data
The middle time history is the wavelet series model
The bottom time history has additional wavelets to improve the SRS match, and it is scaled downward since the El Centro SRS plateau is greater than the specification

## Slide 17: Conclusions
.
The velocity and displacement time histories are well-behaved which is important for both testing and analysis.

## Slide 18: Conclusions
.
The SRS of the modified, synthesized time history is within + 3 dB of the specification
The method is thus successful in generating an El Centro-like time history to meet the specification

## Slide 19: Conclusions
.
Satisfy Same Specification with Alternate Time History
Elegant but does not resemble an earthquake

## Slide 20: Conclusions
.
Alternate Time History SRS
Excellent compliance, but alternate time history still does not resemble an earthquake

## Slide 21: Conclusions
.
Temporal Moment Comparison
Parameter | El Centro Synthesis | Alternate Synthesis
Energy E | 0.0589 | 0.01935
Root energy amplitude Ae | 0.0731 | 0.04754
Central time T (sec) | 13.56 | 9.687
RMS duration D (sec) | 11.02 | 8.562
Central skewness St (sec) | 10.21 | 11.06
Normalized skewness S | 0.9267 | 1.291
Central kurtosis Kt (sec) | 60.13 | 73.67
Normalized kurtosis K | 5.455 | 8.604
The alternate synthesis has about 5 dB less energy and thus may cause an “under test” even though its SRS matches the specification.

## Slide 22: Conclusions
.
22
Second Example Suborbital Launch Vehicle Flight Accelerometer Data

## Slide 23: Conclusions
.
23
Second Example Suborbital Launch Vehicle Flight Accelerometer Data
The Specification is hypothetical, with a plateau of 2000 G and a ramp slope of 9 dB/octave

## Slide 24: Conclusions
.
24
Second Example Wavelet Indirect Approach
A series of five wavelets were combined to represent a 100 Hz, %5 Damped Sine
The individual wavelet frequencies were uniformly scaled to represent damped sines with various frequencies
Use successive groups of frequency-scaled wavelets to add into synthesis process for SRS compliance
Damped sines are more efficient than wavelets for modeling near and mid-field pyrotechnic shock
But damped sines can be modeled via wavelet for desired velocity and displacement control

## Slide 25: Conclusions
.
25
The top time history is the flight accelerometer data
The middle time history is the wavelet series model
The bottom time history has additional wavelets to improve the SRS match, and it is scaled upward since the SRS specification plateau is greater than the flight data
Second Example Suborbital Launch Vehicle Flight Accelerometer Data

## Slide 26: Conclusions
.
26
The velocity and displacement time histories are well-behaved.
Second Example Suborbital Launch Vehicle Flight Accelerometer Data

## Slide 27: Conclusions
.
27
The SRS of the modified, synthesized time history is within + 3 dB of the specification
The method is thus successful in generating a flight-like time history to meet the specification
Second Example Suborbital Launch Vehicle Flight Accelerometer Data

## Slide 28: Conclusions
.
Conclusions
An historical time history can be modified via wavelets to satisfy an SRS specification using a Rube Goldberg approach
The resulting time history will ideally resemble the reference time history, but some amount of distortion must be accepted
The process works more smoothly for SRS specifications that somewhat resemble the reference data SRS
Good topic for case history experiments, further research, etc!

## Slide 29: Conclusions
.
Software
Software and papers for applying this method are freely given at:
http://vibrationdata.wordpress.com/