## Slide 1
Avionics Component Shock Sensitivity
& FEA Shock Analysis
By Tom Irvine
Tutorial & Training Oriented Materials

## Slide 2
https://vibrationdata.wordpress.com/

## Slide 3
Linear Shaped Charge
But fire and smoke would not occur in near-vacuum of space
Plasma jet would occur instead
Metal Clad Linear Shaped Charge
Stage Separation Test

## Slide 4
Vibrationdata
Electronic Boxes
Electronic components in vehicles are subjected to shock and vibration environments
The components must be designed and tested accordingly

## Slide 5
Avionics Component Qualification Testing, Pyrotechnic Excitation
Resonant single or double plate excited by mild detonating cord
Plate made from steel or aluminium
Must over-test in out-of-plane axis in order to meet specification in lateral axis
Used for near-field shock specifications or far-field with very conservative margin

## Slide 6
Vibrationdata
Reference
Steinberg’s text

## Slide 7
Vibrationdata
Circuit Boards & Piece Parts

## Slide 8
Vibrationdata
Solder Joints
Aerospace and military components must be designed and tested to withstand shock and vibration environments
Cracked solder Joints for Piece Part with “J leads”

## Slide 9
Solder Joint & Lead Wire Failures
Adhesive failure and rupture of solder joint after a stringent shock test
Large deflection of PCB resulting from an insufficient support/reinforcement of the PCB combined with high shock loads (above 2000g SRS, depending on the induced PCB deflection), can lead to adhesive failure and rupture of solder joint
Staking needed for parts weighing more than 5 grams

## Slide 10
Solder Joint & Lead Wire Failures (cont)
Sheared lead between solder joint and winding of coil
Lacing cords alone are insufficient
Need lacing plus staking

## Slide 11
Potential Shock Failure Modes
Crystal oscillators can shatter
Large components such as DC-DC converters can detached from circuit boards

## Slide 12
Shock Failure Theories & Proponents
Acceleration – European Space Agency
Pseudo Velocity / Stress – Gaberson
Relative Displacement - Steinberg
Howard A. Gaberson (1931-2013)
Dave S. Steinberg

## Slide 13
Acceleration: Relay Shock Test
Pendulum hammer impact excitation
Relays were powered and monitored
Relay
Accelerometer
Fixture

## Slide 14
Acceleration: Relay Sensitivity from Shock Testing
Note that the levels in the table are maximum values of the time history of the acceleration
The SRS converges to the peak time history acceleration as the natural frequency increases to some high value
EL Series Relay
GP250 Relay

## Slide 15
Acceleration: Part Sensitivity Summary
Electronic Part | Mode 1 | Mode 2 | Mode 3 | Remark
Relays | Bouncing G=200g SRS in all directions | Transfer G=600g SRS in all directions | Mechanical damage G=1200g SRS in all directions | 
Quartz | Relief residual stress G=600 g SRS in all directions | Solder overstress / adhesive crack G=600 g SRS in all directions | Broken crystal 2000 g SRS at quartz resonances | Criteria to be verified with representative Q factors (>100). These values are typical for quartz with frequencies between 50 and 100MHz.
RM, Transformer and Self | 2000 g SRS (above 3000 Hz) | Lead-wire failure Apply stress relief and staking solutions |  | 
Hybrid | Adhesive rupture Design and size dependent | Crack glass feed-thru Design and size dependent | Structural failure Design and size dependent | 
Tantalum capacitor | Local destruction dielectric Capacitor size and PCB deflection dependent – ensure acceptable deflection | Short circuit Capacitor size and PCB deflection dependent – ensure acceptable deflection | Lead-wire failure Apply stress relief and staking solutions | 
Heavy or large component | Heavy component / Lead-wire failure Apply stress relief and staking solutions – ensure acceptable deflection | Large component / Lead-wire failure Design and size dependent – ensure acceptable deflection – apply staking solution |  | 
Optical components (optical fibre connector…) | Fibre pigtail cleavage 2000g SRS (above 2000 Hz) | Damaged fibre 2000 g SRS (above 2000 Hz) |  | 
Low insertion force DIP socket | Disjunction of the component SRS of 1000 to 1300g in OOP |  |  | 
Semiconductors (IC) components, Hybrid components, relays, capacitors with cavities | Dislodging of mobile particle Compare expected levels to the PIND TEST levels if applied, and validate the not covered range of frequencies by the PIND test |  |  | 

## Slide 16
An empirical rule-of-thumb in MIL-STD-810E states that a shock response spectrum is considered severe only if one of its components exceeds the level
Threshold = [ 0.8 (G/Hz) * Natural Frequency (Hz) ]
For example, the severity threshold at 100 Hz would be 80 G
This rule is effectively a velocity criterion
MIL-STD-810E states that it is based on unpublished observations that military-quality equipment does not tend to exhibit shock failures below a shock response spectrum velocity of 100 inches/sec (254 cm/sec)
Equation actually corresponds to 50 inches/sec. It thus has a built-in 6 dB margin of conservatism
Note that this rule was not included in MIL-STD-810F or G, however
Pseudo Velocity: MIL-STD-810E, Shock Velocity Criterion

## Slide 17
The 100 ips limit appears to have been derived from two sources
The first was Gaberson’s shock test of six squirrel cage fans or blowers
The second was a analytical calculation based on the yield stress limit of mild steel
Pseudo Velocity: Historical Notes

## Slide 18
Pseudo Velocity: Historical Notes (cont)
The maximum velocity v max for a given beam undergoing bending vibration is calculated as
σyield | Material yield stress
ρ | Mass per volume
c | Wave speed in the material
k | Constant, for rectangular cross-section
σyield | Material yield stress
ρ | Mass per volume
c | Wave speed in the material
k | 
Mild steel beam: σyield = 33 ksi → v max = 130 in/sec

## Slide 19
Pseudo Velocity: Morse Chart
R. Morse, Spacecraft & Launch Vehicle Dynamics Environments Workshop Program, Aerospace Corp., El Segundo, CA, June 2000

## Slide 20
L
B
Z
Relative Motion
Component
h
Relative Motion
Component
Relative Displacement: Circuit Board and Component Lead Diagram

## Slide 21
Let Z be the single-amplitude displacement at the center of the board that will give a fatigue life of about 20 million stress reversals in a random-vibration environment, based upon the 3 circuit board relative displacement
Steinberg’s empirical formula for Z 3 limit is
Steinberg’s empirical formula for the shock limit is
Z shock = 6 * Z 3σ limit
inches
B | = | length of the circuit board edge parallel to the component, inches
L | = | length of the electronic component, inches
h | = | circuit board thickness, inches
r | = | relative position factor for the component mounted on the board, 0.5 < r < 1.0
C | = | Constant for different types of electronic components, 0.75 < C < 2.25
Relative Displacement: Empirical Fatigue Formula

## Slide 22
.
1.0
0.5
0.707
0.707
Relative Displacement: Position Factor r
r | Component Location (Board supported on all sides)
1 | When component is at center of PCB (half point X and Y)
0.707 | When component is at half point X and quarter point Y
0.5 | When component is at quarter point X and quarter point Y

## Slide 23
C=0.75 | Axial leaded through hole or surface mounted components, resistors, capacitors, diodes
C=1.0 | Standard dual inline package (DIP)
C=1.26 | DIP with side-brazed lead wires
C=1.0 | Through-hole Pin grid array (PGA) with many wires extending from the bottom surface of the PGA
Component Constants

## Slide 24
C=2.25 | 
C=1.26 | Surface-mounted leaded ceramic chip carriers with thermal compression bonded J wires or gull wing wires.
Surface-mounted leadless ceramic chip carrier (LCCC).
A hermetically sealed ceramic package. Instead of metal prongs, LCCCs have metallic semicircles (called castellations) on their edges that solder to the pads.
Component Constants (cont)

## Slide 25
C=1.75 | 
Surface-mounted ball grid array (BGA).
BGA is a surface mount chip carrier that connects to a printed circuit board through a bottom side array of solder balls.
Component Constants (cont)

## Slide 26
Equation for approximating Q for a system is
where | 
A | = 1.0 for beam-type structures
 | = 0.5 for plug-in PCBs or perimeter supported PCBs
 | = 0.25 for small electronic chassis or electronic boxes
fn | Natural Frequency (Hz)
Gin | Sine Base Input (G)
Steinberg Circuit Board Damping Equation

## Slide 27
Steinberg Circuit Board Damping, Sample Cases

## Slide 28
Tom’s Measured Data from Shaker Tests
Range is 9 to 29

## Slide 29
Shock Analysis, Base Excitation
First choice is to model component as an SDOF system
Use FEA for MDOF systems

## Slide 30
MDOF Shock analysis can be performed either as:
1. Time domain modal transient
2. Response spectrum modal combination
Both methods are demonstrated in this presentation
The time domain method requires more computation time but is potentially more realistic
It gives insight into understanding the plausible timing of peaks for individual modes
Allows modal Q values to be different than SRS specification Q value
There are two methods for applying the acceleration as shown on the next page
The indirect seismic mass method is the subject for this presentation
FEA Shock Analysis Introduction

## Slide 31
Acceleration Excitation Methods
31
Assume a rectangular plate mounted via posts at each corner
F
Mount plate to heavy seismic mass via rigid links
Apply force to yield desired acceleration at plate corners
Directly enforce acceleration at corners
For uniform base excitation:
Rigid links

## Slide 32
Time History Synthesis to Meet an SRS Specification
Natural Frequency (Hz) | Accel (G)
100 | 100
2000 | 2000
10,000 | 2000
Typical specification is defined from 100 to 10,000 Hz
Extrapolate down to 10 Hz to cover low frequency modes and for realism
Synthesized acceleration time history and corresponding velocity and displacement should each have zero values for numerical stability

## Slide 33
Damped Sinusoids
Synthesize a series of damped sinusoids to satisfy the SRS
Trial-and-error process with random number generation and convergence
Individual damped-sinusoid
Series of damped-sinusoids
Reconstruct damped sine series via wavelets (non-orthogonal, shaker shock variety)

## Slide 34
Wavelet Equation
Wm (t) = acceleration at time t for wavelet m
Am = acceleration amplitude f m = frequency t dm = delay
Nm = number of half-sines, odd integer > 3

## Slide 35
Typical Shaker-Shock Wavelet
A shock waveform can be modeled by a series of wavelets:
Ferebee R , Irvine T, Clayton J, Alldredge D, An Alternative Method Of Specifying Shock Test Criteria: NASA/TM-2008-215253
Trial-and-error process using random number generation with convergence

## Slide 36
Time History Synthesis Matlab Script
Script included in the Vibrationdata GUI package freely available at: https://vibrationdata.wordpress.com

## Slide 37
The sample rate is 100K samples/sec which is 10 x the highest SRS natural frequency
The time histories is composed of a series of damped sinusoids which have been reconstructed in terms of wavelets
Synthesized Time History

## Slide 38
Maintaining stable velocity & displacement are good engineering practice
Otherwise relative displacement error may occur due to significant digit effects if the displacement has a “ski slope” effect
Matlab: Time History Set

## Slide 39
The synthesized time history satisfies the SRS specification within tolerance bands

## Slide 40
Femap: Plate Nodes, Elements & Corner Constraints
Aluminum 6061-T651
Flat square plate 12 x 12 x 0.25 inch
Constrain all corner nodes for no TX, TY or TZ translation
Node 1201 is at the center in this model
48 elements & 49 nodes per edge
Q=10 for all modes

## Slide 41
Femap: Mode Shape 1
The fundamental mode at 117.6 Hz has 93.3% of the total modal mass in the T3 axis
The plate appears to behave almost as a single-degree-of-freedom system
But higher modes make a very significant contribution to the overall shock response

## Slide 42
Femap: Mode Shape 6
The sixth mode at 723 Hz has 3.6% of the total modal mass in the T3 axis

## Slide 43
Femap: Mode Shape 12
The twelfth mode at 1502 Hz has 1.6% of the total modal mass in the T3 axis

## Slide 44
Femap: Mode Shape 19
The 19th mode at 2266 Hz has only 0.3% of the total modal mass in the T3 axis

## Slide 45
Matlab: Parameters for T3
n | fn (Hz) | Modal Mass Fraction | Participation Factor | Eigenvector at Node 1201 (center) | Eigenvector at Node 49 (mid edge)
1 | 117.6 | 0.933 | 0.0923 | 13.98 | 9.81
6 | 723.6 | 0.036 | 0.0182 | 22.28 | 17.92
12 | 1502 | 0.017 | 0.0123 | 2.499 | -28.5
19 | 2266 | 0.003 | 0.0053 | 32.22 | -16.6
The Participation Factors & Eigenvectors are shown as absolute values
The Eigenvectors are mass-normalized
The Eigenvectors are the only parameter in the table which depends on location
Modes 1, 6, 12 & 19 account for 98.9% of the total mass

## Slide 46
Femap: Synthesized Acceleration Time History
The X-axis is Time (sec)
The Y-axis is Acceleration (in/sec^2)

## Slide 47
Femap: Q Damping
Customize the damping table according to your analysis problem need
Damping can vary with frequency
Q=10 is equivalent to 5% viscous modal damping

## Slide 48
Femap: Node Group
Node 2402
Node 2403
Node 1
Node 49
Node 1201

## Slide 49
Femap: Element Group
Element 50
Element 1129
Node 1201
Run the Nastran modal transient analysis
Post-process the *.f06 file

## Slide 50
Matlab: Vibrationdata GUI, Modal Transient Extraction
Input File: square_plate_modal_transient_seismic_mass.f06
Node 2402 is base drive node

## Slide 51
Matlab: Relative Velocity
Absolute peak: 79.7 in/sec
Absolute peak: 68.9 in/sec
Each peak is below the 100 in/sec threshold

## Slide 52
Absolute peak: 586 G
Absolute peak: 461 G
Matlab: Acceleration

## Slide 53
Matlab: Stress Response, Near Corner, Element 50
The signed Von Mises stress is useful for fatigue analysis
The absolute peak is 7662 psi
Signed Von Mises Stress=
(Von Mises Stress)*sign(Major Principal Stress

## Slide 54
Matlab: Stress Response, Plate Middle, Element 1129
The signed Von Mises stress is useful for fatigue analysis
The absolute peak is 4741 psi

## Slide 55
Matlab: Response Peaks
Peak Absolute Response | Edge Center Node 49 | Plate Middle Node 1201
Relative Displacement (in) | 0.073 | 0.105
Relative Velocity (in/sec) | 68.9 | 79.7
Absolute Acceleration (G) | 586 | 461
The Plate Middle Node has the highest relative displacement & velocity
The Edge Center Node has the highest acceleration
Nodal Response Comparison for T3
Von Mises Stress Response Comparison, unit: psi
Near Corner Element 50 | Plate Middle Element 1129
7662 | 4741

## Slide 56
Modal Combination Methods
Response spectrum analysis is actually an extension of normal modes analysis
ABSSUM – absolute sum method
SRSS – square-root-of-the-sum-of-the-squares
NRL – Naval Research Laboratory method
The SRSS method is probably the best choice for response spectrum analysis because the modal oscillators tend to reach their respective peaks at different times according to frequency
The lower natural frequency oscillators take longer to peak

## Slide 57
where is the mass-normalized eigenvector coefficient for coordinate i and mode j
Conservative assumption that all modal peaks occur simultaneously
These equations are valid for both relative displacement and absolute acceleration
Pick D values directly off of Relative Displacement SRS curve
ABSSUM Method

## Slide 58
These equations are valid for both relative displacement and absolute acceleration
Pick D values directly off of Relative Displacement SRS curve
SRSS Method

## Slide 59
n | fn (Hz) | MMF | PF | Eigen vector | Specification SRS (G) | ¦ PF x Eig x Spec ¦ (G) | ¦ PF x Eig x Spec ¦2 (G2)
1 | 117.6 | 0.933 | 0.0923 | 9.81 | 117.6 | 106.5 | 11339
6 | 723.6 | 0.036 | 0.0182 | 17.92 | 723.6 | 236.0 | 55695
12 | 1502 | 0.017 | 0.0123 | -28.5 | 1502 | 526.5 | 277230
19 | 2266 | 0.003 | 0.0053 | -16.6 | 2000 | 176.0 | 30962
 |  |  |  |  |  | sum = 1045 G | sum = 375,225 G2
 |  |  |  |  |  |  | sqrt of sum = 613 G
This checking method is an approximation for the response of a multi-degree-of-freedom system to an SRS input
The table is taken from the plate model modal analysis results prior to the addition of the seismic mass, with three added columns
The set composed of modes 1, 6, 12 & 19 accounts for almost 99% of the total mass
The seventh column is the participation factor times the eigenvector times the SRS specification
The sum of the absolute responses is 1045 G, which conservatively assumes that each mode reaches its peak at the same time as the others
The “square root of the sum of the squares” is 613 G
The FEA modal transient peak response was 586 G which passes the “sanity check”
Acceleration Response Check for Mid Edge Node 49 T3

## Slide 60
n | fn (Hz) | MMF | PF | Eigen vector | Specification SRS (G) | ¦ PF x Eig x Spec ¦ (G) | ¦ PF x Eig x Spec ¦2 (G2)
1 | 117.6 | 0.933 | 0.0923 | 13.98 | 117.6 | 152 | 23104
6 | 723.6 | 0.036 | 0.0182 | -22.28 | 723.6 | 293 | 85849
12 | 1502 | 0.017 | 0.0123 | 2.499 | 1502 | 46 | 2116
19 | 2266 | 0.003 | 0.0053 | 32.22 | 2000 | 342 | 116964
 |  |  |  |  |  | sum = 833 G | sum = 228033 G2
 |  |  |  |  |  |  | sqrt of sum = 478 G
The table is taken from the plate model modal analysis results prior to the addition of the seismic mass, with three added columns
The sum of the absolute responses is 833 G, which conservatively assumes that each mode reaches its peak at the same time as the others
The “square root of the sum of the squares” is 478 G
The FEA modal transient peak response was 461 G which passes the “sanity check”
Acceleration Response Check for Center Node 1201 T3

## Slide 61
Matlab Command Window >> spec=[10 10; 2000 2000; 10000 2000]
Vibrationdata SRS Modal Combination

## Slide 62
Vibrationdata SRS Modal Combination Results, Center Node 1201 T3
SRS Q=10
fn(Hz) Accel(G)
10.0 10.0
2000.0 2000.0
10000.0 2000.0
fn Q=10
(Hz) SRS(G)
117.6 117.6
723.6 723.6
1502 1502
2266 2000
fn Part Eigen SRS Modal Response
(Hz) Factor vector Accel(G) Accel(G)
117.6 0.0923 13.98 117.6 151.7
723.6 0.0182 -22.28 723.6 293.4
1502 0.0123 2.499 1502 46.17
2266 0.0053 32.2 2000 341.3
ABSSUM= 832.7 G SRSS= 477.2 G

## Slide 63
E | Elastic modulus
ρ | Mass per volume
[Vn]max | Modal velocity
The stress [σn]max for mode n is:
Stress-Velocity Equation
Ĉ is a constant of proportionality dependent upon the geometry of the structure, often assumed for complex equipment to be 4 < Ĉ < 8
Ĉ ≈ 2 for all normal modes of homogeneous plates and beams

## Slide 64
Matlab: Vibrationdata Shock Toolbox

## Slide 65
Matlab: MDOF SRS Stress Analysis for Node 1201
Matlab Command Window >> spec=[10 10; 2000 2000; 10000 2000]
The peak velocity response occurs at center Node 1201
The peak stress occurs near each of the four corners
The stress-velocity calculation accounts for this difference

## Slide 66
Matlab: Peak MDOF SRS Stress from Node 1201 velocity
The peak FEA response spectrum stress for the whole plate was 7662 psi
FEA stress passes sanity check, but a lower Ĉ value may be justified so that the SRSS agrees more closely with the FEA results
SRS Q=10
fn(Hz) Accel(G)
10.0 10.0
2000.0 2000.0
10000.0 2000.0
fn Q=10
(Hz) SRS(G)
117.6 117.6
723.6 723.6
1502 1502
2266 2000
fn Q Part Eigen Accel PV SRS Modal Response
(Hz) Factor vector SRS(G) (in/sec) Stress(psi)
117.6 10 0.0923 13.98 117.6 61.43 8070
723.6 10 0.0182 -22.28 723.6 61.43 2536
1502 10 0.0123 2.499 1502 61.43 192.2
2266 10 0.0053 32.2 2000 54.22 942
ABSSUM= 11740 psi SRSS= 8513.1 psi
Hybrid Gaberson Stress-Velocity Relationship

## Slide 67
Unit 201
Nastran FEA Base Excitation Response Spectrum

## Slide 68
Introduction
Shock and vibration analysis can be performed either in the frequency or time domain
Continue with plate from Unit 200
Aluminum, 12 x 12 x 0.25 inch
Translation constrained at corner nodes
Mount plate to heavy seismic mass via rigid links
Use response spectrum analysis
SRS is “shock response spectrum”
Compare results with modal transient analysis from Unit 200
The following software steps must be followed carefully, otherwise errors will result
Rigid links

## Slide 69
Femap: Add Constraints to Current Constraint Set
All DOF fixed except TZ

## Slide 70
Femap: Create New Constraint Set Called Kinematic

## Slide 71
Femap: Add Constraint to Kinematic Set
Constrain TZ
The seismic mass is constrained in TZ which is the response spectrum base drive axis

## Slide 72
fn (Hz) | Peak Accel (G)
10 | 10
2000 | 2000
10000 | 2000
Shock Response Spectrum Q=10
Good practice to extrapolate specification down to 10 Hz if it begins at 100 Hz
Because model may have modes below 100 Hz
Aerospace SRS specifications are typically log-log format
So good practice to perform log-log interpolation as shown in following slides
Go to Matlab Workspace and type:
>> spec=[10 10; 2000 2000; 10000 2000]

## Slide 73
Femap: View Response Spectrum Function
Change title from TABLED2 to SRS_Q10

## Slide 74
Femap: Define Response Function vs. Critical Damping
For simplicity, the model damping and SRS specification are both Q=10 or 0.05 fraction critical
Function 7 is the SRS specification
Specifications for other damping values could also be entered as functions and referenced in this table, as needed for interpolation if the model has other damping values
Multiple SRS specifications is covered in Unit 202

## Slide 75
Femap: Define Normal Modes Analysis with Response Spectrum

## Slide 76
Femap: Define Normal Modes Analysis Parameters
Solve for 20 modes

## Slide 77
Femap: Define Nastran Output for Modal Analysis

## Slide 78
Femap: SRS Cross-Reference Function
This is the function that relates the SRS specifications to their respective damping cases
“Square root of the sum of the squares”
The responses from modes with closely-spaced frequencies will be lumped together

## Slide 79
Femap: Define Boundary Conditions
Main Constraint function
Base input constraint, TZ for this example

## Slide 80
Femap: Define Outputs
Get output f06 file
Quick and easy to output results at all nodes & elements for response spectrum analysis
Only subset of nodes & elements was output for modal transient analysis due to file size and processing time considerations

## Slide 81
Femap: Export Nastran Analysis File
Export analysis file
Run in Nastran

## Slide 82
Matlab: Vibrationdata GUI

## Slide 83
Matlab: Nastran Toolbox

## Slide 84
Matlab: Response Spectrum Results from f06 File

## Slide 85
Matlab: Response Spectrum Acceleration Results
Center node 1201 has T3 peak acceleration = 475.9 G from response spectrum analysis
Modal transient result from Unit 200 was 461 G for this node

## Slide 86
Node 1201
Node 49
Matlab: Response Spectrum Acceleration Results (cont)
Center node 1201 had T3 peak acceleration = 475.9 G
Edge node 49 had highest T3 peak acceleration = 612.5 G
By symmetry, three other edge nodes should have this same acceleration
But node 1201 had highest displacement and velocity responses

## Slide 87
Matlab: Response Spectrum Results - SRSS
Maximum Displacements:
node value
T1: 2376 0.00000 in
T2: 931 0.00000 in
T3: 1201 0.10746 in
R1: 1 0.02054 rad/sec
R2: 1 0.02054 rad/sec
R3: 1 0.00000 rad/sec
Maximum velocities:
node value
T1: 2376 0.000 in/sec
T2: 931 0.000 in/sec
T3: 1201 83.665 in/sec
R1: 1 20.246 rad/sec
R2: 1 20.246 rad/sec
R3: 1 0.000 rad/sec
Maximum accelerations:
node value
T1: 2376 0.000 G
T2: 931 0.000 G
T3: 49 612.541 G
R1: 1 116739.700 rad/sec^2
R2: 1 116739.700 rad/sec^2
R3: 1 0.000 rad/sec^2
Maximum Quad4 Stress:
element value
NORMAL-X : 1105 6047.053 psi
NORMAL-Y : 24 6047.053 psi
SHEAR-XY : 50 4798.865 psi
MAJOR PRNCPL: 24 6047.816 psi
MINOR PRNCPL: 1128 4997.801 psi
VON MISES : 50 8400.833 psi

## Slide 88
n | fn (Hz) | PF | Eigen vector | Q | Interpolated SRS (G) | ¦ PF x Eig x Spec ¦ (G) | ¦ PF x Eig x Spec ¦2 (G2)
1 | 117.6 | 0.0923 | 13.98 | 10 | 117.6 | 151.7 | 23027
6 | 723.6 | 0.0182 | -22.28 | 10 | 723.6 | 293.4 | 86093
12 | 1502 | 0.0123 | 2.499 | 10 | 1502 | 46.2 | 2131
19 | 2266 | 0.0053 | 32.22 | 10 | 2000 | 341.5 | 116644
 |  |  |  |  |  | sum = 833 G | sum = 227896 G2
 |  |  |  |  |  |  | sqrt of sum = 477 G
Acceleration Response Check for Node 1201 T3
Center node 1201 had T3 peak acceleration = 475.9 G from the FEA SRSS
The FEA value passes the modal combination check

## Slide 89
Vibrationdata GUI

## Slide 90
Vibrationdata Shock Toolbox

## Slide 91
>> spec=[10 10; 2000 2000; 10000 2000]
Vibrationdata SRS Modal Combination

## Slide 92
Vibrationdata SRS Modal Combination Results
SRS Q=10
fn(Hz) Accel(G)
10.0 10.0
2000.0 2000.0
10000.0 2000.0
fn Q=10
(Hz) SRS(G)
117.6 117.6
723.6 723.6
1502 1502
2266 2000
fn Part Eigen SRS Modal Response
(Hz) Factor vector Accel(G) Accel(G)
117.6 0.0923 13.98 117.6 151.7
723.6 0.0182 -22.28 723.6 293.4
1502 0.0123 2.499 1502 46.17
2266 0.0053 32.2 2000 341.3
ABSSUM= 832.7 G SRSS= 477.2 G

## Slide 93
n | fn (Hz) | PF | Eigen vector | Q | Interpolated SRS (G) | ¦ PF x Eig x Spec ¦ (G) | ¦ PF x Eig x Spec ¦2 (G2)
1 | 117.6 | 0.0923 | 9.81 | 10 | 117.6 | 106.5 | 11339
6 | 723.6 | 0.0182 | 17.92 | 10 | 723.6 | 236.0 | 55695
12 | 1502 | 0.0123 | -28.5 | 10 | 1502 | 526.5 | 277230
19 | 2266 | 0.0053 | -16.6 | 10 | 2000 | 176.0 | 30962
 |  |  |  |  |  | sum = 1045 G | sum = 375225 G2
 |  |  |  |  |  |  | sqrt of sum = 613 G
Acceleration Response Check for Node 49 T3
Edge node 49 had T3 peak acceleration = 612.5 G from the FEA SRSS
The FEA value passes the modal combination check

## Slide 94
Femap: T3 Acceleration Contour Plot, unit = in/sec^2
Import the f06 file into Femap and then View > Select

## Slide 95
Femap: T3 Velocity Contour Plot, unit = in/sec

## Slide 96
Femap: T3 Translation Contour Plot, unit = inch
This is actually the relative displacement

## Slide 97
Matlab: Response Spectrum Stress Elements
Element 50 had the highest Von Mises stress = 8401 psi
Element 1129 had Von Mises stress = 5001 psi
Element 50
Element 1129
Node 1201
Node 101

## Slide 98
Matlab: Response Spectrum Stress Results

## Slide 99
Femap: Von Mises Stress Contour Plot

## Slide 100
Matlab: Vibrationdata Shock Toolbox

## Slide 101
Matlab: MDOF SRS Stress Analysis for Node 1201
The peak velocity response occurs at center Node 1201
The peak stress occurs near each of the four corners
The stress-velocity calculation accounts for this difference

## Slide 102
E | Elastic modulus
ρ | Mass per volume
[Vn]max | Modal velocity
The stress [σn]max for mode n is:
Stress-Velocity Equation
Ĉ is a constant of proportionality dependent upon the geometry of the structure, often assumed for complex equipment to be 4 < Ĉ < 8
Ĉ ≈ 2 for all normal modes of homogeneous plates and beams

## Slide 103
Matlab: Peak MDOF SRS Stress from Node 1201 velocity
SRS Q=10
fn(Hz) Accel(G)
10.0 10.0
2000.0 2000.0
10000.0 2000.0
fn Q=10
(Hz) SRS(G)
117.6 117.6
723.6 723.6
1502 1502
2266 2000
fn Q Part Eigen Accel PV SRS Modal Response
(Hz) Factor vector SRS(G) (in/sec) stress(psi)
117.6 10 0.0923 13.98 117.6 61.43 8070
723.6 10 0.0182 -22.28 723.6 61.43 2536
1502 10 0.0123 2.499 1502 61.43 192.2
2266 10 0.0053 32.2 2000 54.22 942
ABSSUM= 11740 psi SRSS= 8513.1 psi
The peak FEA response spectrum stress for the whole plate was 8401 psi
FEA stress passes sanity check, but a lower Ĉ value may be justified so that the SRSS agrees more closely with the FEA results