## Slide 1
SDOF Response to White Noise Base Input Rainflow Statistical Study Revision A
By Tom Irvine
May 17, 2021

## Slide 2
Introduction
Consider a random base input to a spring-mass, single-degree-of-freedom (SDOF) system with a given natural frequency and amplification factor
The base input may either be a time history or a power spectral density (PSD)
The first step is to calculate the absolute acceleration response of the system ẍ for a given input ÿ, either in the time or frequency domain
The Smallwood ramp invariant digital recursive filtering relationship is used in the time domain
The middle step in the time domain is to perform a rainflow cycle count using ASTM E 1049-85 (2005), section 5.4.4
The rainflow cycles are then input to a Miners-type cumulative damage index summation to calculate the relative damage for a given fatigue exponent using a Basquin approach where the fatigue S-N curve is assumed to be a straight line in log-log format

## Slide 3
Introduction (cont)
For the frequency domain analysis, the textbook power transmissibility function is used for the response calculation
The semi-empirical Dirlik method can be used for the equivalent rainflow cycle counting and relative damage summation in the frequency domain, which will be considered in the follow-on analysis
The Dirlik equation is based on the weighted sum of the exponential, and two Rayleigh distributions

## Slide 4
Objective
The purpose of this analysis is to consider the statistical variation of the damage index for the time domain analysis using a white noise base input
The resulting damage index is shown to have an approximate lognormal distribution
This information can be used to predict normal tolerance limits for the relative damage index
Future research will be performed to derive an estimated standard deviation for the relative damage via a simple formula instead of using a vast number of time domain trials

## Slide 5
Numerical Study
The following study is performed using one million runs
A unique white noise time history is generated for each run
The sample rate is 10 kHz with a duration of 300 sec and a standard deviation of 1 G
Note that the standard deviation and RMS values are the same for a mean value of zero
The white noise time history is band-limited via its sample rate
The white noise time history by nature is stationary with a normal distribution
The SDOF oscillator has a natural frequency of 500 Hz and a amplification factor of Q=10
Two fatigue exponents are used b=4 & 8
The relative damage index is calculated for each of the runs and for each fatigue exponent

## Slide 6
SDOF Response, Frequency Domain

## Slide 7
Relative Damage Results for fn=500 Hz, Q=10, b=4
Parameter | Log10 | Linear
Mean (G4) | 6.44 | 2.76e+06
Std Dev (G4) | 0.004348 | 2.76e+04
RMS (G4) | 6.44 | 2.76e+06
Min (G4) | 6.420 | 2.63e+06
Max (G4) | 6.462 | 2.90e+06
Skewness | 0.00240 | 0.0324
Kurtosis | 2.997 | 2.998
The skewness is improved by modeling the distribution as lognormal
The levels from the lognormal approach are:
P99/90: 2.82e+06 G4
P01/90: 2.69e+06 G4
These level can be used as the respective upper and lower relative damage estimates for the b=4 case

## Slide 8
Relative Damage Results for fn=500 Hz, Q=10, b=8
Parameter | Log10 | Linear
Mean (G8) | 8.485 | 3.06e+08
Std Dev (G8) | 0.0130 | 9.20e+06
RMS (G8) | 8.485 | 3.06e+08
Min (G8) | 8.426 | 2.67e+08
Max (G8) | 8.594 | 3.92e+08
Skewness | 0.0843 | 0.1767
Kurtosis | 3.048 | 3.100
The skewness and kurtosis are improved by modeling the distribution as lognormal
The levels from the lognormal approach are:
P99/90: 3.28e+08 G8
P01/90: 2.85e+08 G8
These level can be used as the respective upper and lower relative damage estimates for the b=8 case

## Slide 9
Appendix A, Fatigue Damage Spectra, Lognormal Mean
The calculation was repeated for a family of natural frequencies at 1/12 octave spacing
100 runs were performed per each natural frequency