## Slide 1: Unit 17
SDOF Response to Applied Force Revision A

## Slide 2: Introduction
SDOF systems may be subjected to an applied force
Modal testing, impact or steady-state force
Wind, fluid, or gas pressure
Acoustic pressure field
Rotating or reciprocating parts
  Rotating imbalance
  Shaft misalignment
  Bearings
  Blade passing frequencies
  Electromagnetic force, magnetostriction

## Slide 3: SDOF System, Applied Force
m | = | mass
c | = | viscous damping coefficient
k | = | stiffness
x | = | displacement of the mass
f(t) | = | applied force

## Slide 4: Free Body Diagram
Summation of forces
Solve using Laplace transform.
f(t)
m
kx

## Slide 5
For an arbitrary applied force, the displacement x is
Smallwood-type, ramp invariant, digital recursive filtering relationship
T = time step

## Slide 6: SDOF Acceleration
For an arbitrary applied force, the displacement is

## Slide 7: Time Domain Calculation for Applied Force
Let
fn = 10 Hz
Q=10
mass = 20 lbm
Calculate response to applied force:
F = 4 lbf, freq = 10 Hz, 4 sec duration, 400 samples/sec
First: vibrationdata > Generate Signal > Sine Export time history as: sine_force.txt
Next: vibrationdata > Select Input Data Type > Force
> Select Analysis > SDOF Response to Applied Force

## Slide 8: Applied Force Time History

## Slide 9: Displacement

## Slide 10: Transmitted Force
Special case:
SDOF driven at resonance
Transmitted force
= ( Q )( applied force )

## Slide 11: Synthesize Time History for Force PSD
Similar process to synthesizing a time history for acceleration PSD.
But the integrated force time history does not need to have a mean value of zero.
Frequency (Hz) | Force (lbf^2/Hz)
10 | 0.1
1000 | 0.1
Duration = 60 sec

## Slide 12: Synthesized Time History for Force PSD
vibrationdata > Power Spectral Density > Force > Time History Synthesis from White Noise
f = 4.26 Hz
Export as:
force_th.txt

## Slide 13: Histogram of Force Time History

## Slide 14: PSD Verification

## Slide 15: SDOF Response
Let
fn = 400 Hz
Q=10
mass = 20 lbm
Calculate response to the previous synthesized force time history.
vibrationdata > Select Input Data Type > Force
> Select Analysis > SDOF Response to Applied Force

## Slide 16: Displacement
Export:
disp_resp_th.txt
Overall Level =
7.4e-05 in RMS

## Slide 17: Velocity
Export array:
vel_resp_th.txt
Overall Level =
0.18 in/sec RMS

## Slide 18: Acceleration
Export array:
accel_resp_th.txt
Overall Level = 1.3 GRMS
Crest Factor = 5.0
Theoretical Rayleigh Distribution
Crest Factor = 4.6

## Slide 19: Transmitted Force
Export array:
tf_resp_th.txt
Overall Level =
24.3 lbf RMS

## Slide 20: Frequency Response Function
Dimension | Displacement/Force | Velocity/Force | Acceleration/Force
Name | Admittance, Compliance, Receptance | Mobility | Accelerance, Inertance
Dimension | Force/Displacement | Force/Velocity | Force/Acceleration
Name | Dynamic Stiffness | Mechanical Impedance | Apparent Mass, Dynamic Mass

## Slide 21: FRF Estimators
Cross spectrum between force and response divided by autospectrum of force
Cross spectrum is complex conjugate of first variable Fourier transform times the second variable Fourier transform.
* Denotes complex conjugate
The response can be acceleration, velocity or displacement.

## Slide 22: FRF Estimators (cont)
Autospectrum of response divided by cross spectrum between response and force
Coherence Function  is used to assess linearity, measurement, noise, leakage error, etc. Coherence is ideally equal to one.

## Slide 23: Frequency Response Function Exercise
Calculate mobility function (velocity/force) using:
vibrationdata > miscellaneous > modal frf
- Two separate Arrays – Ensemble Averaging
Arrays: force_th.txt & vel_resp_th.txt
df = 3.91 Hz & use Hanning Window Important!
Plot H1 Freq & Mag & Phase

## Slide 25: Mobility H1 SDOF fn=400 Hz, Q=10
Save Complex Array:
H1_mobility _complex.txt

## Slide 26: Mobility H2 SDOF fn=400 Hz, Q=10

## Slide 27: Coherence from Mobility
Coherence = 0.98
at 400 Hz

## Slide 28: Estimate Q from H1 Mobility, Curve-fit
vibrationdata > Damping Functions > Half-power Bandwidth Curve-fit, Modal FRF
H1_mobility _complex.txt
fn=400 Hz
Q=10.1

## Slide 29: Homework
Repeat the examples in the presentation using the Matlab scripts
Read:
  T. Irvine, Machine Mounting for Vibration Attenuation, Rev B, Vibrationdata, 2000
  Bruel & Kjaer Booklets:
  Mobility Measurement
  Modal Testing